## Slide 1: Naco Gliderpage – http://naco.gfi.uib.no/gp
A tool for piloting Seagliders from web-clients
or: HowTo avoid learning vi

## Slide 2: Naco Gliderpage - developed at Geophysical Institute, UoB Norway
Web-client tool based on Google Maps API v.3
Integration of Google Maps and free wms/gis map-layers from statkart.no/geonorge.no, ngdc.noaa.gov (gebco08) and arcgisonline.com
Integration of Google Maps and weather data from Norwegian met.office: met.no/yr.no
Integration between the map-application, tech. matlab plots, communication towards the basestation for editing cmdfile/science/target, download of data- and logfiles, update from recent dive and monitoring tech. health of gliders .
Developed in javascripts, html, python and matlab

## Slide 3: Naco Gliderpage versions:
Gliderpage Pro pilot version
  https - userid & password login required
  Sync towards the seaglider basestation
Glider page public version (http://naco.gfi.uib.no/gp)
  http – general public access
  Pilot functions disabled (no editing of essential files)
  Sync towards Pro pilot web-server
Gliderpage Pro pilot backup/dev server.
Near identical configurations.

## Slide 4: Naco Gliderpage Web-client tool advantages:
  All necessary applications integrated into one interface and one application
  No «tech applications» like ssh/sftp/winscp/vi
  allows «non-tech» seaglider pilots.
  - No local matlab or python installations
  (all run by scripts on web-server)
  Entire group of pilots, scientists and the public
  access data and figures from the same interface.
  Reliable and stable. Free for the glider community.

## Slide 5: Naco Gliderpage:
Google Maps Api v.3
  High quality global & regional maps
  Well known and flexible interface
  Google maps elevation service
  Easy access to WMS and GIS-layers
  (WMS- web map server, GIS – Geogr. information services)
Drawback: Google Maps use a variant of the mercator projection (EPSG:3857). Operations deep into the polar ice require polarstereographic projections and probably OpenLayer maps

## Slide 6: Gliderpage – maps

## Slide 7: Gliderpage – Regional multibeam echosound + contour maps

## Slide 8: Gliderpage – National Geograph. maps

## Slide 9: Gliderpage – Gebco08 maps

## Slide 10: Gliderpage – pilot functions
Glider pilot functions
- Essential file editor
Next Dive - Edit:
CMDFILE, SCIENCE,
TARGET, BAT
Every Dive - Read:
Comm.log, Capture
*.LOG *.ENG
dive.txt

## Slide 11: Gliderpage – pilot functions
GaaG – Glider at a Glance
  Monitor Glider tech. health

## Slide 12: Gliderpage – tech. plots for pilot control

## Slide 13: Gliderpage – Custom plots
Plots any pair of seaglider parameters for a series of dives

## Slide 14: Google maps++: Ruler tool, Elevation services & depth contours

## Slide 15: Gliderpage – weather data from met.no

## Slide 16: Gliderpage – Enhancements in progress
Ice charts
  For ice edge operations
Wave & wind charts
  Model forecasts from met.no

## Slide 17: Gliderpage – Enhancements in progress
Regional current models
  Model prognosis from met.no

## Slide 18: Gliderpage – Enhancements in progress
- Custom science plots
  Based on Python
  Future: Gliderpage Slocum module?
  Other groups may have other solutions and preferences.
  More alternatives/Better ideas - «Let the flowers bloom»
  Collaborative ideas are welcome!

## Slide 19
Notes: Våre skip går til lands og til vanns – og i lufta med!

## Slide 20: Gliderpage – New vs Old map

## Slide 21: Gliderpage – depth average current vs depth profile

## Slide 22: Gliderpage – editing cmdfile/targets, surveillance of tech health