## Slide 1: Coupled physical and phytoplankton dynamics in Antarctic coastal seas
Filipa Carvalho, Josh Kohut, Oscar Schofield, Max Gorbunov
Center for Ocean Observing Leadership,
Rutgers University, USA
7th EGO Meeting
September 29th, 2016
Matthew Oliver
College of Earth, Ocean and Environment, University of Delaware, USA

## Slide 2: WAP Canyons are “Biological Hotspots”
Palmer Deep Canyon
(Palmer LTER site)
Eveleth et al., 2016
“Biological Hotspots” along the Peninsula associated with deep undersea canyons.
Penguin Colonies at coastal termini of cross-shelf canyons/troughs
Predictable / elevated food availability;
Increased phytoplankton concentration at canyon heads;
Patterns variable in space/time

## Slide 3: WAP deployments: focusing on the Palmer Deep Canyon
~30 000 CTD glider profiles
~6 000 FIRe glider profiles
In the Canyon alone,
(2010-2015)
PHYSICAL DIVERS OF THE BLOOM
Notes: Deploying since 2007,
More regular since 2010.

## Slide 4: Seasonal cycle at Palmer Deep Canyon (WAP) Shallow MLD + increased stratification = increased chlorophyll
Carvalho et al, 2016 (JGR)
Temperature
Stratification
Salinity
Chlorophyll
Notes: Gliders high res data allows us to capture the phytoplankton dynamics and characterize

## Slide 5: Seasonal cycle at Palmer Deep Canyon (WAP) Shallow MLD + increased stratification = increased chlorophyll
Carvalho et al, 2016 (JGR)
Temperature
Stratification
Salinity
Chlorophyll
Glacial
meltwater
Sea-ice
meltwater
Increased
stratification
Increased
biomass
Shallow
MLD
Notes: Gliders provide high resolution data that allow us to look at the seasonal cycle and understand when and where these patches of phytoplankton occur.
But now we are interested in understanding WHY by looking at their state and how healthy they are. And look at a much smaller timescale and see even see how the daily light variation affect them.
Physiology!!

## Slide 6: Current phytoplankton physiology measurements methods
Discrete Sampling
Fluorescence Induction and Relaxation (FIRe) Benchtop
Continuous surface sampling
Phytoplankton health
Notes: Chl-a Fluorescence is our proxy for biomass.
Light affects physiology, Surface has too much light
therefore fluorescence measurements affected, and will not coincide with actual biomass (underestimates)
Discrete – constrains: water collection capabilities and manpower (run samples manually)

## Slide 7: Fluorescence Induction and Relaxation Sensor
FIRe glider
Using gliders to map phytoplankton physiology
Notes: Providing continuous and high resolution mapping in depth of the phytoplankton physiological responses to light stress using fluorescence kinetics,

## Slide 8: FIRe Glider 101
comprehensive suite of photosynthetic and photo-physiological characteristics in high temporal/spatial resolution.
Notes: By using a series of flashes of know intensity, duration and interval, we can evaluate …
indication on the efficiency of photosynthetic light-harvesting processes
info used to assess environmental stresses (as nutrient limitation and photoinhibition)

## Slide 9: FIRe Glider 101
comprehensive suite of photosynthetic and photo-physiological characteristics in high temporal/spatial resolution.
Fm = maximum Fluorescence (proxy for biomass)
Fo = minimum Fluorescence
σPSII = functional absorption cross section of PSII
Fv = variable fluorescence (Fm-Fo)
Fv/Fm = Photosynthetic efficiency or quantum yield of
photochemistry in PSII [(Fm-Fo)/Fm]
(phytoplankton health)

## Slide 10: “Healthy” Phytoplankton have higher Fv/Fm
Increasing Fv/Fm
Notes: In very broad terms,
It tells us how efficient they are at using the light available to photosynthesize.

## Slide 11: Cross-calibration between instruments
Satlantic Desktop FIRe
Webb-Satlantic FIRe glider
PAR
FIRe
Satlantic Benchtop FIRe
Webb-Satlantic FIRe glider
Notes: processing

## Slide 12: WAP deployments: focusing on the Palmer Deep Canyon
~30 000 CTD glider profiles
~6 000 FIRe glider profiles
PHYSICAL DIVERS OF THE BLOOM
In the Canyon alone,
(2010-2015)

## Slide 13: WAP deployments: focusing on the Palmer Deep Canyon
~30 000 CTD glider profiles
~6 000 FIRe glider profiles
PHYTOPLANKTON PHYSIOLOGY
In the Canyon alone,
(2010-2015)

## Slide 14: 2 Missions designs
Temporal evolution
“Drift mission”
Spatial variability
“Station keeping mission”
Notes: Not only, gliders sample at the right scales, but also allow us to adapt our sampling to our science questions.

## Slide 15: 2 Missions designs
Temporal evolution
“Drift mission”
Spatial variability
“Station keeping mission”
Goal: Evaluate the physiology of the same phytoplankton community through time
Follow the same water mass
Corkscrew dive every hour
Drift while at the surface
Diel cycles
Comparison between different MLD regimes
Goal: Evaluate physiological responses to different physical forcing
Continuous sampling at the same location (<500 m radius)
FIRe profile every hour
Pitch adjusted to increase vertical resolution
Notes: Different phytoplankton species and different communities of the same species react differently to light.
Phytoplankton adapt to mid light level they are exposed

## Slide 16: Evaluating spatial variability: Regional comparison
Important variables:
Salinity
Water masses present
Stratification
MLD
Ocean currents
Storms (mixing)
phytoplankton
biomass
phytoplankton
health
Notes: Station keeping mission
Main goal was to evaluate how phytoplankton react to different physical forcing.
simultaneous high res sampling of FIRe with physical parameters measured by gliders and other instruments such as salinity ….
Connection Allows us to identify which parameters are stressors and drivers of phytoplankton.

## Slide 17
Phytoplankton health
Biomass
Temperature
MLD
Diel cycles show evidence of Non-Photochemical Quenching (NPQ)
Notes: Drift mission
Accompanying the same water mass through time
MLD changes through time
Changes in physiology under different MLD regimes

## Slide 18: Diel cycles show evidence of Non-Photochemical Quenching (NPQ)
Comparison between different MLD – evaluation of photoacclimation regimes
Higher NPQ signal in deeper MLD regimes – low light acclimation
Phytoplankton health
Biomass
Temperature
MLD
Notes: Both cases, evidence of NPQ (or less happy phytoplankton) during highest irradiance times.
But higher NPQ signal in deeper MLD regime
Indicating low light acclimation

## Slide 19: Mixed Layer Depth (MLD): important parameter for Phytoplankton.
Gille, 2010 (Nat. Geosci.)
Well-lit
Zone
Important metric in phytoplankton studies + stratification
Light levels available to phytoplankton resulting from MLD affect physiology
MLD = Homogeneous layer in upper ocean
MLD
Notes: The depth of the ML can regulate the amount of solar radiation available to the phytoplankton community
MLD is shallow, phytoplankton stay within the well-lit zone, where they thrive. High light level acclimation
MLD is deep, phytoplankton are distributed over a larger volume of water, and sink more easily to depths too dark to sustain them.
From below, water column stability at the base of the ML has been linked to the flux of nutrients to the surface layer, replenishing surface blooms with important nutrients for primary production

## Slide 20
MLD
Modeling physiological response to light forcing
Notes: Take a step further

## Slide 21
MLD
Modeling physiological response to light forcing
Notes: and model how phytoplankton respond to light in timescales of hours (over a diel cycle)

## Slide 22
MLD
Modeling physiological response to light forcing
Phytoplankton health
Phytoplankton health
Notes: Use the power relationship observed between PAR (photosynthetic available radiation) and our phytoplankton health
And apply that to a model

## Slide 23
MLD
Ek=197
Ek=336
Ek=63
Ek=165
Ek=272
Ek=289
Ek=233
Ek=238
MLD
PAR>40
10-20m
PAR>40
0-10m
PAR<40
0-10m
PAR<40
10-20m
surface
deep
Modeling physiological response to light forcing
Notes: Then we can go even further and compare the response of phytoplankton at different depths throughout the diel cycle to understand how phytoplankton acclimate to light in order to thrive

## Slide 24
MLD (m) | Shallow (  16) | Deeper (  32)
Stratification max[N2], s-2 | High (  2x10-3) | Low (  6.7x10-4)
Biomass (FIRe Fm’) | Higher | Lower
Layer 0‑10m | High-light acclimated (higher Ek) | Mid-light (MLD) acclimated Ek (0-10m)  Ek (10-20m)
Layer 10‑20m | Low-light acclimated (lower Ek) | 
MLD (m) |  | 
Stratification max[N2], s-2 |  | 
Biomass (FIRe Fm’) | Higher | Lower
Layer 0‑10m | High-light acclimated (higher Ek) | Mid-light (MLD) acclimated Ek (0-10m)  Ek (10-20m)
Layer 10‑20m | Low-light acclimated (lower Ek) | 
MLD
MLD
PAR>40
10-20m
PAR>40
0-10m
PAR<40
0-10m
PAR<40
10-20m
surface
deep
Ek=197
Ek=336
Ek=63
Ek=165
Ek=272
Ek=289
Ek=233
Ek=238
Top plot
Bottom plot
Modeling physiological response to light forcing
Notes: Shallow MLD, different layers with different light acclimations
While in dee MLD, we are able to capture the phytoplankton acclimating at a mid-water light level

## Slide 25: Fluorescence Quenching Correction
Use backscatter when available (high correlation in Antarctic waters)
NPQ

## Slide 26: NPQ corrections in chlorophyll fluorescence (using backscatter)
Backscatter
CHL Fluorescence
Corrected CHL Fluorescence
Carvalho et al, 2016 (JGR)
R2=0.885

## Slide 27: NPQ corrections in chlorophyll fluorescence (using backscatter)
R2=0.885
NPQ
Backscatter
CHL Fluorescence
Carvalho et al, 2016 (JGR)

## Slide 28: NPQ corrections in chlorophyll fluorescence (using backscatter)
NPQ
Backscatter
CHL Fluorescence
Corrected CHL Fluorescence
R2=0.885
Carvalho et al, 2016 (JGR)

## Slide 29: Future work: Fluorescence Quenching Correction
Use night profiles to correct daytime profiles (assuming same water mass)
FIRe glider with Fluorescence and Backscatter puck

## Slide 30: Conclusions
Gliders provide high-res water column biophysics
Integration of a FIRe sensor into a glider allows us to map, with high temporal and spatial resolution, phytoplankton physiological responses to physical forcing
Glider data allow modeling of phytoplankton light response at the right scales
Future work: NPQ correction using night profiles

## Slide 31: Thank You!
Filipa Carvalho
filipa@marine.rutgers.edu

## Slide 32: Phytoplankton in the WAP
Courtesy of Zina Deretsky / NSF

## Slide 33: FIRe post processing
Gain correction
Blank correction
Convert FIRe Fm into chlorophyll-a concentration

## Slide 34: Slocum Gliders
AUV; 1.5 meter; ~ 60 kg
Buoyancy driven (saw-tooth pattern)
Sensors: CTD (Temperature, Salinity, Depth), Fluorescence, Backscatter, Oxygen, ADCP, FIRe & PAR
But why use gliders??
Notes: Gliders are 1.5 m long torpedo-shaped, winged Autonomous Underwater Vehicles (AUVs). They are Integrated instrument platforms designed to operate in coastal areas and oceanic regions. Here we have a top view schematics of a glider. The tail here has all communication antennas, here is the air bladder that inflates when the glider is at the surface to facilitate the communications, main computer in the aft section, science payload in the middle. Batteries in the front section together with the pump. The pump is what makes the glider fly. They are buoyancy-driven with a saw tooth-shaped gliding trajectory. The gliders are neutrally buoyant in the water. In the front section, a pump will retract, diminishing the glider’s volume. Less volume with the same mass means higher density, so the glider sinks. On the contrary, when the pump expels the water from the front compartment, the glider becomes less dense, and consequently positively buoyant and floats. And because it has wings, this vertical movement is transformed into a horizontal movement and so it moves slowly forward at a speed around 0.35 m/s.

## Slide 35
MLD
MLD vs. photoacclimation regimes

## Slide 36
MLD
MLD vs. photoacclimation regimes

## Slide 37
MLD
MLD vs. photoacclimation regimes

## Slide 38: Slocum Gliders
AUV; 1.5 meter; ~ 60 kg
Buoyancy driven (saw-tooth pattern)
Sensors: CTD (Temperature, Salinity, Depth), Fluorescence, Backscatter, Oxygen, ADCP, FIRe & PAR
High-resolution sampling
Long endurance

## Slide 39: Antarctic Glider Deployments
 | # deployments | # Profiles | # Days
WAP | 26 | 16 673 | 407
Ross Sea | 3 | 2 212 | 67
Amundsen Sea | 3 | 2 247 | 26

## Slide 40: Seasonal cycle at Palmer Deep Canyon (WAP) Shallow MLD + increased stratification = increased chlorophyll
Carvalho et al, 2016 (JGR)
Increased
stratification
Increased
biomass
Notes: Gliders provide high resolution data that allow us to look at the seasonal cycle and understand when and where these patches of phytoplankton occur.
But now we are interested in looking at their state and how healthy they are. And look at a much smaller timescale and see even see how the daily light variation affect them.