## Slide 1
Understanding Turbulent Controls On The Ocean Surface Boundary Layer With The Ocean Microstructure Glider
Matthew Palmer
Chris Balfour, MARS glider team
Mark Inall, Holly Pelling, Jeff Polton, Jo Hopkins, Juliane Wihsgott, Charlotte Williams, Holly Pelling etc.
See Hopkins et al, poster Thursday

## Slide 2
The Ocean Microstructure Glider OMG
but….
So accurately resolving flow past the sensor (U) is vital since ε scales with 1/U4
U
ui

## Slide 3: OMG: Flight model (Merckelbach et al, 2010)
Where Vg = 56.075 ×10-3m3
mg = 57.56 kg
A = 0.1m2
and ΔVbp & θ from sensors
CD0 and CD1 are drag coefficients (due to parasitic and induced drag) dependent on α
G = mixing efficiency
U
w
θ
α
θ
α
Accounting for the angle of attack, α
γ
Total glide angle,
We employ the hydrodynamic flight model of Merckelbach et al, 2010;
Balancing buoyancy and gravitational forces

## Slide 4: Using a flight model to constrain CD0 and α
G = mixing efficiency
Minimising difference between measured and modeled vertical velocity;
-
0
CD0,down = 0.2070 (±2%)
CD0,up = 0.2065 (±2%)
CD0 ~0.2066
Estimate α iteratively using prescribed values for the lift-slope coefficients (ah and aw) and the induced drag CD1
For further information see Palmer et al,
J. Marine Systems (144)
available at noc.ac.uk/people/rolm/

## Slide 5: FASTNEt Ocean shelf exchange experiments:
2013: Malin Sea
OMG was deployed for 14.8 days alongside station SF which provides ADCP and ‘Wirewalker’ CTD.
OMG provides 1869 profiles of the TKE dissipation rate (ε), fast T and CTD, typically every 11 minutes.
Ocean Microstructure Glider

## Slide 6: OMG Malin Sea: Measuring within the turbocline
Storm mixing
Steady deepening of the surface mixed layer
130m

## Slide 7: Surface forcing
Met forcing provided by nearby RRS James Cook.
Wave data from tri-axis wavebuoy.
Buoyancy flux +ve with heat loss from the ocean
Turbulent Langmuir number Lat;
Lat2 = u*/uS

## Slide 8: Working towards parameterisation of the Ocean Surface Boundary Layer (OSBL)
Belcher et al, GRL 2012
Regime diagram relates ε to h/Ll and La,
La = u* / uS (uS = Stokes drift)
Ll = -w3*L / Bs
w3*L = u*2uS
La represents the balance between wind and waves,
h/Ll represents the balance between wave and buoyancy forcing
Wave

## Slide 9: Relative contributions to surface forcing from wind, waves and convection
Comparing non-dimensionalised εh/u*3 (z/h = 0.5) to Lat
Lat = 0.3
Lat = 0.4
v Bs > 0
^ Bs < 0

## Slide 10: Depth dependency of turbulence during wind and wave dominated periods
OMG provides valuable validation of law-of-the-wall scaling.
During wave-convective case turbulence scales by (kUs)3 and shows no depth dependence
Wind driven regime
Wave driven regime

## Slide 11: Working towards parameterisation of the Ocean Surface Boundary Layer (OSBL)
Data shows generally good agreement with Belcher et al, GRL 2012
Waves
Wind
Convection
Increased ε relative to h/LL suggests the need for an additional wave dependent term in the convective regime.
Wave

## Slide 12: Conclusions
A new 15 day time-series from an OMG provides unprecedented access to turbulent controls of the (very) shallow near surface layer.
The vast majority of data are confined to a narrow band of Lat ∼0.3, Lat <0.3 occurred only 25% of the time and Lat <0.20 occurred only 5% of the time.
During periods when Lat  0.3, turbulence is shown to be accurately predicted by u⋆3/h, decaying with depth following the law of the wall.
When waves dominate (i.e. Lat <0.3), turbulence is accurately scaled by k.uS3/h, and follows a near constant distribution over h, where k is suggested to be a near constant O[0.1].
Our Lat <0.3 data however, coincides with a convective event. We therefore suggest that this relationship offers a potential for improved parameterisation for wave-convection interaction in the OSBL. Further validation is required.

## Slide 13: Coming soon: Celtic Sea 2015