## Slide 1
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations
Gustavo Jorge Goni1
Francis Bringas1
Ricardo Domingues2,1
Jili Dong 2,1
Grant Rawson2,1
Ulises Rivero1
Thomas Sevilla2,1
Julio Morell3
George Halliwell1
Sang-Ki Lee1
Hyun-Sook Kim4
Luis Pomales3
Becky Baltes5
Richard Bouchard6
Yamil Rodriguez7
1 NOAA Atlantic Oceanographic and Meteorological Laboratory - AOML, Miami, Florida, USA
2 University of Miami, Cooperative Institute for Marine and Atmospheric Studies - CIMAS, Miami, Florida, USA
3 University of Puerto Rico, Mayagues, Puerto Rico, and Caribbean Coastal Ocean Observing System - CARICOOS
4 NOAA Environmental Modeling Center , College Park, Maryland, USA
5 NOAA Integrated Ocean Observing System – IOOS, Silver Spring, MD, USA
6 NOAA National Data Buoy Center, Stennis, Miss, USA
7 Autoridad Nacional de Asuntos Maritimos - ANAMAR, Dominican Republic

## Slide 2
Tropical Cyclone Intensity and Track Forecasts Error
NHC Official Track Error - Atlantic
North Atlantic Statistics
11 named Tropical Cyclones
6 Hurricanes (winds > 64 kt)
2-3 Major Hurricanes (winds > 96 kt, cat3)
Major Hurricane History
Cat5: > 137 kt
Cat4: 113 – 136 kt
Cat3: 96 – 112 kt
Cat2: 83 – 95 kt
Cat1: 64 – 82 kt

## Slide 3
Tropical Cyclone Intensity and Track Forecasts Error
NHC Official Intensity Error - Atlantic
NHC Official Track Error - Atlantic

## Slide 4
Role of the Ocean in Tropical Cyclone Intensification
Rapid Intensification of Hurricane Katrina (2005)
Katrina (2005) intensified rapidly from category 3 into a category 5 hurricane in less than 12 hours as it travelled over a warm ocean eddy
Other examples:
Opal (1995) [Shay et al., 2000]
Ivan(2004), Wilma (2005) [Mainelli et al., 2008]

## Slide 5
World Ocean Atlas 2013: # of Temperature profiles
1955-2012
Number of obs.
< 200
2005-2012
PR
DO
Need for UOHC obs.!
Network of gliders to carry out sustained and targeted ocean observations in the Caribbean Sea and Tropical North Atlantic in support of hurricane studies and forecasts

## Slide 6
Goal
Enhance our understanding of air-sea interaction processes during hurricane force wind events.
Objectives
Assess impact of hurricane force winds on upper ocean density structure, and
Assess impact of ocean profile data from underwater gliders in hurricane intensity forecasts.
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations

## Slide 7
Supported by:
Disaster Relief Appropriations Act of 2013 (Sandy Supplemental funds, 2014-2015)
NOAA AOML (present)
NOAA IOOS and CARICOOS (present)
NOAA OAR AAA Reserve 2015 and 2016 (present)
NOAA NDBC (present)
  http://www.aoml.noaa.gov/phod/gliders
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations

## Slide 8
Seaglider™
  4 vehicles
Sensors
  CT Sail or GPCTD
    Temperature & Salinity
  Aandera Oxygen Optode
    Dissolved Oxygen
  Wetlab - ECO Triplet
    Chlorophyll-a
    CDOM
    Backscatter (700 nm)
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations

## Slide 9
Glider Port at UPRM, Puerto Rico
NOAA AOML
UPRM
NOAA-AOML
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations

## Slide 10
Hurricane Season Deployments
July-November
Objective: carry out ocean observations in support of Hurricane studies and forecasts
Off-Hurricane Season Deployments
February-June
Objective: carry out ocean observations to improve understanding of the variability of the physical and chemical parameters in the Caribbean Sea
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations
PR
PR

## Slide 11
Other remote and in-situ observations: targeted ocean observations (AXBTs, AXCTDs,..), Argo floats, surface drifters, satellite sea surface temperature and sea height.
TS Bertha
(August, 2014)
Hurricane Gonzalo
(October, 2014)
First mission
Jul-Nov 2014
Second mission
Feb-Apr 2015
Third mission
Jul-Nov 2015
Fourth mission
March – June 2016
5 missions, 20 months of observations, approximately 10,000 T, S profiles to date
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations

## Slide 12
5 missions, 20 months of observations, approximately 10,000 T, S profiles to date
Mission 5
(Underway)
July 2016 – present
Hurricane Season Deployment
4 Gliders Deployed
  2 in the Caribbean Sea
  2 in the Tropical North Atlantic
~3,000 profiles of each parameter:
  T & S
  Dissolved Oxygen
  Chlorophyll-a
  CDOM
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations
Mission 5

## Slide 13
Mission 5: Current Meteorological Conditions
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations
Mission 5

## Slide 14
Data Distribution
PHOD/AOML website
  http://www.aoml.noaa.gov/phod/gliders
  Real-time location
  Plot of glider observations
  Individual T, S & DO profiles
  Data Access
Global Telecommunication System – GTS
  Assimilated into forecasting systems
NOAA’s Integrated Ocean Observing System - IOOS
  http://www.ioos.noaa.gov/
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations
NOAA NCEI
NOAA OSMC
NCEI – National Centers for Environmental Information
OSMC – Observing System Monitoring Center

## Slide 15
Summary:
Underwater gliders can provide critical temperature and salinity profile data in real-time even during tropical cyclone wind conditions.
Over 10,000 profiles of each observed parameter, such as temperature, salinity, dissolved oxygen, and chlorophyll concentration have been collected during the first two years of the NOAA/AOML-CARICOOS Hurricane Underwater Glider Operations
One case study, with significant results during Hurricane Gonzalo (2014), indicates that glider data improves ocean initialization when assimilated within HYCOM-HWRF model.
Future work:
Continue collecting ocean profile data, with enhanced glider network.
Assess optimal observational strategy to improve TC intensity forecast using a suite of ocean observations.
Further collaboration with other institutions interested in monitoring the UOHC in support of Tropical Cyclone intensification studies and forecasts
Domingues, R., G. Goni, F. Bringas, S.-K. Lee, H.-S. Kim, G. Halliwell, J. Dong, J. Morell, and L. Pomales (2015), Upper ocean response to Hurricane Gonzalo (2014): Salinity effects revealed by targeted and sustained underwater glider observations, Geophys. Res. Lett., 42, doi:10.1002/2015GL065378.
Dong et al, Impact of underwater glider data on Hurricane Gonzalo (2014) forecast, 2016, to be submitted.

## Slide 16
Future Work

## Slide 17
NOAA/AOML – CARICOOS Hurricane Underwater Glider Operations
Gustavo Jorge Goni1
Francis Bringas1
Ricardo Domingues2,1
Jili Dong 2,1
Grant Rawson2,1
Ulises Rivero1
Thomas Sevilla2,1
Julio Morell3
George Halliwell1
Sang-Ki Lee1
Hyun-Sook Kim4
Luis Pomales3
Becky Baltles5
Richard Bouchard6
Yamil Rodriguez7
1 NOAA Atlantic Oceanographic and Meteorological Laboratory - AOML, Miami, Florida, USA
2 University of Miami, Cooperative Institute for Marine and Atmospheric Studies - CIMAS, Miami, Florida, USA
3 University of Puerto Rico, Mayagues, Puerto Rico, and Caribbean Coastal Ocean Observing System - CARICOOS
4 NOAA Environmental Modeling Center , College Park, Maryland, USA
5 NOAA Integrated Ocean Observing System – IOOS, Silver Spring, MD, USA
6 NOAA National Data Buoy Center, Stennis, Miss, USA
7 Autoridad Nacional de Asuntos Maritimos - ANAMAR, Dominican Republic
Thank you
Gustavo.Goni@noaa.gov