## Slide 1: Slocum Fleet Mission Control Advanced Glider Piloting Tools
Ben Allsup, Clayton Jones & Chris DeCollibus

## Slide 2
There are the updated global pictures from the remote sensors on satellites, there the evolving maps of subsurface variables, there the charts that show the position and status of all our Slocum scientific platforms, and I am satisfied that we are looking at the ocean more intensely and more deeply than anyone anywhere else.
- Dr. Henry Stommel The Slocum Mission, 1989

## Slide 3: History
Gliders communicate to a server on shore through a satellite connection routed to either a static IP address or a landline. A “Dockserver” application was created to allow pilots to interact with gliders when connected and in mission so the gliders can be monitored and controlled.
Traditional Java Dockserver tools:
Glider Terminal
  Text-based glider communication
Data Visualizer
  MySQL database
GLMPC Terminal
  Mapping and Waypoint tool
FTP client
  Used to send files to/from glider

## Slide 4: Limitations of Existing Tools
All 4 tools require Java and are only compatible with Windows or Linux.
Single level of security
Outdated
Lack rapid visibility to glider/fleet status
No pilot note keeping system
GLMPC Tool
  Allowed for a location plotting of a single vehicle only.
  Cut and paste map of .jpg images are hard to use and do not allow the user to zoom.

## Slide 5: Objectives of New Tools
Ability to easily Pilot and Monitor Multiple Vehicles
Access the tools from any platform (PC, MAC, tablet, smartphone)
Increase security
Allow for collaboration between multiple pilots.
Allow for roles: Admin, pilot and viewer only accounts
Combine the functionality of the old tools into a single application.
Leverage and optimize existing tools and visualizations.

## Slide 6
Continuing to Partner with colleagues in Education and Industry

## Slide 7: Slocum Fleet Mission Control (SFMC)

## Slide 8: Features: User Accounts
Increased Access Control
Individual user accounts with different roles:
  Admin
  Group Admin
  Pilot
  Viewer
Customizable Group Assignments
  Gliders and User are linked to groups.

## Slide 9: Glider Monitoring :Dashboard

## Slide 10: Dashboard : Deployment Status
Connection status
Time Connected
Last connection time and date
Speed over ground
Next waypoint, and distance to waypoint.
Dockserver script status
Near real time updates
Direct link to terminal session with the glider

## Slide 11: Dashboard: Alerts: New email notification capability on alerts

## Slide 12: Dashboard: Comms Plot
  Shows the connection times of individual gliders
  Allows user to click on a particular surface event and download the corresponding surface log file.

## Slide 13: Dashboard: Maps
  Shows Multiple glider deployment
  Features:
    Zoom to selected deployment
    Full Screen
    Change track color
    Hide Glider icon overlay
    Time Slider
    Overlays
      Base Map cutomization
      User overlays (WMS)

## Slide 14
Dashboard: Maps

## Slide 15: Deployment View
Summary: a status bar
Map: single glider
Surfacings
Surface Sensor Values

## Slide 17: Deployment View: Summary and Notes
Summary:

## Slide 18: Deployment View: Surfacings
  - Similar to the Summary Bar, but includes information on all glider surfacing's
  - Easily search surfacing's by date
  - Includes link to download the log files from the indivual surfacing.

## Slide 19: Deployment View: Surface Sensors
  Allows user to easily track and monitor sensors that are included in their surface dialog
  Individual users can set upper and lower limits for each sensor which can trigger alerts if they are exceeded.
  Sensor Plotting:
    Surface sensors can quickly be plotted over time.
    A delta/hr can be applied to allow the user to see what their normal run rate is.

## Slide 20: Terminal

## Slide 21: Terminal
Terminal Status Bar
Includes:
  Glider name
  The script name, status and state
  Script controls
  Connection type and port information
  Other users who are viewing this terminal
Glider Connection Area:
  Shows status of other gliders that are currently connected to this Dockserver
  Shows status of other gliders that have connected to this Dockserver in the past

## Slide 22: Terminal: Command Entry
Shows Recent Commands. Includes Date and User Name
Uses browser command recall

## Slide 23: File Transfer
File transfers can now be done straight from the Terminal Page (drag and drop)
Easy access to the To-Glider, From-Glider, Logs, and Archive directories.
Click on the title to open a search box which easily sorts through data.
Files can be individually downloaded right from this search or entire sets can be downloaded as a zip file.
FTP no longer needed

## Slide 24: Waypoint planning

## Slide 25: Iphone and Tablet
shot here

## Slide 26: System Specifications
Web based tool
Backend: developed with Java
Frond-end: Developed using HTML5 and Javascript.
There is no Java dependency for client usage.
Data base switched over from MySQL to PostgresQL.
Compatible with existing Dockserver hardware

## Slide 27: Services - Hosting
TWR Hosted SFMC Server (Primary or Backup)
  SSAE 16 Type II compliant facility located in Rockland, MA
  RUDICS capability
  Redundant internet
  Redundant power
  - Multiple redundant phone lines and modems - reliable (99.9% uptime) - secure - fault-tolerant
  Server has easy access from North Falmouth Facility however not on Cape Cod
  - rsync capability upon request

## Slide 28: Services Piloting Training
Primary, Emergency support and back up
Dedicated piloting room
Training Center
Dedicated server(s)
TWR has over 5 decades of Glider piloting experience on staff
Over a year of “glider days” in 2016 to date

## Slide 29: Future
Web based data visualizer replacement.
Mission Planning.
And More!
Available for quote and shipping with new orders now.
Looking for user feedback.