## Slide 1
KUGON
Korea Underwater Glider Operation Network
JongJin Park and DongYoung Kim
Center for Autonomous Best-Integrated Surveillance System
Kyungpook National University

## Slide 2: KUGON
Korea Underwater Glider Operation Network
Purpose :
Building infrastructure for
glider operation
Any necessary work for operational
use of glider
(Optimizing glider missions to
reduce operation risk)
Goal:
Replacing and improving regular
ship-based measurements
Initiating integrated autonomous
marine observation and surveillence
system

## Slide 3: Needs of KUGON Project
Tough marine environment for Autonomous Glider Operation
Various types of
fishing activity
Complex ship traffic
Various and energetic current system
Operation Risk Management is necessary!
Woods Hole (US)
South Korea
< Fishing gears in Korea >
< Comparison of ship traffic between
US and Korea >
< 80m
~150m
> 2000m
< Geometry around
the Korean Peninsula >
Notes: 크레인으로 내리는 사진..

## Slide 4: Operation Risk Management
Concept of Operation Risk Management
Current Environment
Fishery Environment
Ship Traffic
Environment
Optimized
Mission Design
Goal Setting
Operation
Risk
Evaluation
Don’t
GO
GO-
Don’t GO
Decision
GO
Griffiths and Trembranis (2006)
Optimizing Data Transfer Cycle,
Route & Diving Depth Setting,
Contents of Data Transfer,
Observation Cycle and etc.
Optimized Mission Design using Operational Risk Analysis
Feedback
Operation Environment
Analysis

## Slide 5: Glider-Ship Collision Probability Model
Glider-Ship Collision Probability Model
Based in Kaplan-Meier Survival Model
Glider-Ship Collision Probability in the specific area(1km×1km) cell
[Ship Traffic Density Distribution (unit: ships per day per km2)
and Virtual Glider Trajectory]

## Slide 6: Fisheries of the Korea Ocean
Risk by Fisheries
Seasonal Risk Calculation
Seasonal Risk
Investigating the Number of Fishing vessels
Total Number of Fishing Vessels by Fishery Type and Fishing Location
[Total Number of Line fishing Vessels]
[Total Number of Grillnet Vessels]
The information of fishing activities is not
enough. Difficult to predict the risk by fishing.
The most important risk management work is to drink with local fishermen!

## Slide 7: Current of the East Sea
(a)U030m
Prevalence (%)
(b)U200m
Prevalence (%)
(c)U400m
Prevalence (%)
Current prevalence estimates from 13 year-long HYCOM Reanalysis Data
Occurrence Probability of currents stonger than 0.25m/s
Gliders in the southern part of the East/Japan Sea should dive deeper than 400m at least!

## Slide 8: Selecting glider YO pattern
2 multi-YOs
Ulleungdo
Dokdo
Y (km)
10
0
-10
-20
3 multi-YOs
Ulleungdo
Dokdo
Y (km)
10
0
-10
-20
Vertical Route – Ocean Scale
Needs of optimizing Vertical Route
- To Increase spatial resolution of data as well as
to reduce the number of surfacings
Maximum Diving Depth using Ocean Scale
Surrounding the Ulleungdo in the East Sea
Maximum Diving Depth + Number of Multiple YOs
5 multi-YOs
Ulleungdo
Dokdo
X (km)
Y (km)
10
0
-10
-20
-30
0 20 40 60
<Glider trajectory simulation
using HYCOM Reanalysis Data>

## Slide 9: Ulleungdo – Dokdo Field Test
First Sea Trial of KUGON
June 24th - July 18th (25 days)
Test List
  Basic Flight Test
  Butterfly Route Flight Test
  Ulleungdo-Dokdo Round Trip
  (Virtual Mooring Test)

## Slide 10: Ulleungdo – Dokdo Field Test
Butterfly Test & Ulleungdo-Dokdo Round Trip Test
Total Travel Distance : 150 km
Total Travel Time : 191 hours (8 days)
Diving Depth : 400 m ~ 800 m
Total Travel Distance : 17 km
Total Travel Time : 25 hours
Diving Depth : 400 m

## Slide 11: Ulleungdo – Dokdo Field Test
Virtual Mooring Test
Salinity
Total Travel Time : 45 hours
Diving Depth : 300 m
Temperature
(Anomaly)

## Slide 12: Benefits to other major programs
Korea Underwater Glider Operation Network
KODC(Korea Oceanographic Data Center)
Regular Ship-based Measurement Program
Increasing demand for Higher Spatio-temporal Resolution of Oceanographic data
Medium Altitude UAV
Geosynchronous Satellite
SAR and Optical Satellite
Low Altitude UAV
Airship
AUV
HF Ocean Radar
Program for Wide-Integrated Surveillance System of Marine Territory
Building 3-Dimensional Autonomous
Marine Surveilance System (~$100M)

## Slide 14: Possible Integration with Argo Floats
Best testbed for integration with Argo floats and underwater glider fleet
High Argo Data Density!
Argo float in East Sea
Argo float data
(1999~2015)
Argo float location
(21 floats active in Jan. 2016)
The East/Japan Sea
Deploying about
5-10 floats every year
Similar thermo-haline
circulation to open ocean
(including its own MOC)
-> Best testbed to develop ways to integrate with Argo floats and Glider fleets
Yet, still sparse within 10 days!

## Slide 15: Simulator
Underwater Glider Simulator Model
Simulator
Current
Database
Mission Setting
Value
Bathymetric
Data
Glider
Flight Model
Navigation Model
(Current Correction)
Traffic volume
of vessels,
Fisheries Data
Development Procedure

## Slide 16: Simulator
Horizontal Movement Simulator
Error Rate
Prototype Simulator
HYCOM
Current Data
Dead-reckoning
Algorithm
Horizontal Speed
Diving Depth
Single or Multi Dive
Time to Stay on the Surface
Waypoints
Simple
Flight Model

## Slide 17: Compass Calibration
Dimensions | 1360mm(L)×1280mm(W)×780mm(D)
Mass | About 40kg
Material | Aluminium, Brass, MC Nylon
Detail | Heading 360°, Pitch ±30°, Separable
Compass Calibrator
360°
±30°

## Slide 18: Compass Calibration
Compass Calibration
Calibration start
Confirm error
Measure compass error
Compass calibration
Calibration finish
Apply result
(Bias correction)
Preparations
Compass accuracy
check
Compass calibration
× 3 (normal heading,
pitch, pitch-roll)
Random error variance
Error 1% ↑
Error 1% ↓
Set calibrator
Mount glider
Calibrated!
Adjust Horizontality