## Slide 1: Workshop: Turbulence Measurements with the MicroRider
Southampton, England
Date: September 29, 2016
Chair: Fabian Wolk
fabian@rocklandscientific.com

## Slide 2: Who We Are
Cumulative Experience
  50 years in oceanographic turbulence research
  22 years in oceanographic instrumentation
  > 50 publications on turbulence measurements
Team
  16 full-time staff / + students
  Oceanographers
  Mechanical / Electronics Engineers
  Software Developers
  Technologists
  Administration
Location
  Victoria, B.C. Canada
Focus
Turbulence measurements and instrumentation

## Slide 3: Why Ocean Turbulence is Important
Climate Change: Understand ocean circulation.
  Mixing Processes affect the exchange of heat, salt and momentum.
Global Heat Transport
  50 per cent of the pole-ward transport of heat is in the ocean.
  Turbulence affects ocean-atmosphere exchange processes
  Affects rates of ice melt
Anthropogenic impact
  Local changes to water stratification affect wildlife and fisheries
  Resource extraction (minerals, energy, etc.) requires environmental impact assessment
Notes: Why should we care about Ocean Turbulence?

## Slide 4: Emerging Applications
Tidal Energy Conversion
  Site characterization
  Device-resource interaction
  Array layout optimization
Offshore Mining
  Manganese nodule mining
  Tailings disposal
Oil & Gas
  Pollution propagation measurement & modelling

## Slide 5: The MicroRider
Notes: What is the platform for the shear probe?

## Slide 6: MicroRider integrations
2008 Slocum
2014 Seaglider
2016 SeaExplorer
Notes: What is the platform for the shear probe?

## Slide 7: The Velocity Shear Probe
Notes: How can we measure ocean turbulence?

## Slide 8: The Velocity Shear Probe
+ Extremely sensitive, high signal-to-noise ratio
+ Low power
Must move through the water
Resolves only cross-stream velocity fluctuations
Notes: How can we measure ocean turbulence?

## Slide 9: Scale Resolution
L ~ 0.01 m
Wavenumber resolution:
L ~ 2 m

## Slide 10
Figure by T. Hibiya (2008)

## Slide 11: Data Recording
Environmental Signal
e.g.: velocity, temperature, micro-conductivity
Sensor (transducer)
e.g., shear probe
Analog to Digital conversion
Binary data file recorded
Signal conditioning (pre-emphasis)
Analog signal out
DAT_013.p file
16 bit

## Slide 12: Signal Conditioning (Temperature)
Signal pre-emphasis
  Combine signal with it’s own time derivate, e.g. T+ G dT/dt
  Must be done before digitization
T
T + G dT/dt

## Slide 13: Signal Conditioning
Signal pre-emphasis, with high analog noise level

## Slide 14: Data Processing
Binary Data File
DAT_013.p
De-emphasize and convert to physical units
i.e., temperature in deC
Signal Cleanup
High-pass filter
Calculate dissipation rate
Epsilon
Removal of vibration
Removal of spikes

## Slide 15: Signal Cleanup: De-spiking
Spikes occur in the data from impact with plankton or debris
Spikes need to be removed to avoid bias of spectrum (spectral “whitening”)

## Slide 16: Signal Cleanup: Vibration removal

## Slide 17: Vibration signatures

## Slide 18: Data processing
pitch

## Slide 19: EM Flow sensor for MicroRiders
Nemo Turbulence Float
TWR Slocum Glider

## Slide 20: OMG: Flight model (Merckelbach et al, 2010)
Where Vg = 56.075 ×10-3m3
mg = 57.56 kg
A = 0.1m2
and ΔVbp & θ from sensors
CD0 and CD1 are drag coefficients (due to parasitic and induced drag) dependent on α
G = mixing efficiency
U
w
θ
α
θ
α
Accounting for the angle of attack, α
γ
Total glide angle,
We employ the hydrodynamic flight model of Merckelbach et al, 2010;
Balancing buoyancy and gravitational forces

## Slide 21: Using a flight model to constrain CD0 and α
G = mixing efficiency
Minimising difference between measured and modeled vertical velocity;
-
0
CD0,down = 0.2070 (±2%)
CD0,up = 0.2065 (±2%)
CD0 ~0.2066
Estimate α iteratively using prescribed values for the lift-slope coefficients (ah and aw) and the induced drag CD1

## Slide 22: Data Products

## Slide 25: Case Study 1: Celtic Sea, Matthew Palmer
9 days (near) continuous microstructure time-series.
766 profiles of ε and CTD.
Resolving finescale temperature, density and turbulent structure.

## Slide 26: Case Study: Faroe Straight (Ilker Fer)

## Slide 27: Ocean Microstructure Glider Workshop
Day 1 – technical overview and setup
Introduction to the MicroRider
Data Acquisition Software (ODAS5IR)
Pre-deployment Checks
Day 2 – field test
Glider field deployment
MicroRider Maintenance (optional)
Day 3 – data acquisition and processing
Data Conversion and Processing
Signal Conditioning
Day 4 – special topics

## Slide 28
March 5-8, 2017
Honolulu, Hawaii
following the ASLO Aquatic Sciences Meeting (Feb 27-Mar 3, 2017)

## Slide 29: Summary
Gliders are an excellent platform for ocean turbulence measurements., because their are driven by buoyancy.
Dissipation rates resolved ε ~10-8 to ε ~ 5 x 10-11 W/kg, meets open-ocean requirements.
Glider measurements reveal new physical processes that cannot be observed from ship borne measurements.
Next: on-board data processing
Thank you.